## Slide 1: Unit - 4 Telecommunications and Network
Introduction to telecommunications
Telecommunication refers to all types of data transmission, from voice to video. people need to exchange data & information electronically with each other. Telecommunication is the sending of information in any form from one place to another using electronic media.
OR
The transformation of data(text,images,voice,graphics etc.) over different media from one set of electronic devices from another.
The concept of a network
Two or more computers are connected together to form a network.

## Slide 2: Advantages
It provides cheaper and faster communication services.
It is easy to share the resources like software ,data ,hardware ,network etc.
It provides faster and cheaper data transmission between multiple computers.
It uses a tool for e- mail, chat, face book, videoconferencing which facilitates communication.
It provides centralized administration and control.

## Slide 3: Disadvantages
It increases the cost.
It cannot maintain and control the privacy of the people.
High chances of spreading the viruses through network.
It is very complicated for use and maintenance.
Well trained technical person or expertise is required.

## Slide 4: Analog & digital signals
Analog signals are just like longitudinal wave or continuous data signals. It follows wave in continuous ways. As for example temperature, pressure, current, voltage etc.
Digital signals are like traverse wave or discrete or discontinuous data signals. It follows wave in discontinuous ways.

## Slide 5: Modulation
The process of changing some characteristics( amplitude, frequency or phase) of a carrier wave in accordance with the intensity of the signal is known as modulation. Simply modulation means to change attributes.
Need for modulation
Antenna length
Operating range
Wireless communication

## Slide 6
Antenna length
In order to transmit a wave effectively, the length of the transmitting antenna should be approximately equal to the wavelength of the wave.
Operating range
The energy of the wave depends upon its frequency. The greater the frequency of the wave, the greater the energy possessed by it. Audio frequency are small they cannot be transmitted over long distances.

## Slide 7
3. Wireless communication
To modulate a high frequency carrier wave with the audio signal & permit the transmission to occur at this high frequency.

## Slide 8: Types of modulation
Amplitude modulation(AM)
When the amplitude of high frequency wave is changed in accordance with the intensity of signal is called amplitude modulation. It describes the depth of modulation.
Frequency modulation(FM)
When the frequency of the wave is changed in accordance with the intensity of the signal it is called the F.M.F.M. changes only frequency.
Phase modulation(PM)
PM is a change in the carrier phase angle. The phase angle cannot change without affecting a change in frequency.

## Slide 9: Modem
The modem stands for modulator/demodulator. A modem is a device which translates data from digital or binary code(0 or 1) to analog data that can be transmitted over the telephone network.
Transfer speeds
The speed at which the modems can transfer data is measured in bits per second (bps).Internet transfer rates range 14.4kbps, 28.8kbps, 33.6kbps & 56 kbps etc are available.

## Slide 10: Computer connecting media or devices are
Computers
Server
Clients
NIC(network cards) Network interface card is essential to connect the computers using communication media.
Communication media
The path to transfer data from one computer to another computer is called communication media. There are two types of communication media.
Bounded media
Unbounded media

## Slide 11
Bounded media are twisted pair, co-axial cable, fiber optics cable etc.
Unbounded media are Wi-Fi, microwave, satellite, Bluetooth etc.
4. Network connecting devices are Hub, Switch, Bridge and repeaters etc.
Repeaters: These are the signal amplifier used to amplify weak signal and increase length of LAN. It links similar LAN’s. When networking operating system(NOS) are similar for any two or more LAN then these LAN’s are called similar LAN’s.

## Slide 12
Bridge: It is a store and forward device used to connect different or similar networks(LAN).
Local Bridge
Remote Bridge
Router : It is a highly intelligent , protocol sensitive linking device used to link similar or dissimilar LAN’S. A router which can be hardware, software or both.
Gateway: It is used to link dissimilar LAN’s. It also performs all functions of bridge and router . It is slower than bridge and router because it converts entire protocol of one network to other. Gateway converts Ethernet protocol into token ring protocol.

## Slide 13
Hubs: Hub is used to receive incoming data, amplify and distribute. Hub is used as a central component of star topology.
Types of telecommunication:
Telephone networks
PBX
ISDN
Other types
LAN
WAN
MAN

## Slide 14
3. On the basis of its geographical locations
Pear to pear network
Client server network
Telephone network
Private Branch Exchanges(PBX)
A private branch exchange is an electronic switching device(or a special computer), located within the company ,that automatically switches calls between the company’s telephone lines. A PBX performs a number of functions, such as call routing, call forwarding , storing, redialing.

## Slide 15
Integrated services digital network(ISDN)
ISDN is a high speed, fully digital telephone service just like discs. ISDN upgrades analog telephone network to digital system. ISDN can operate at speeds up to 128 kilobits/second which is five or more times faster than the modems. ISDN can dramatically speed up transfer of information over the internet.

## Slide 16: 2. On the basis of its geographical locations
LAN(Local Area Network) : LAN is relatively small. It contains within department, building or college . Its range is 1 km (up to 5 km.
MAN(Metropolitan Area Network): MAN is a network that is large than a LAN. MAN is a network that share some characteristics of both LAN and MAN. MAN usually cover a wider geographical area ( up to 50 km) than LAN. It is located in city or metropolitan area.
WAN(Wide Area Network): A WAN includes all networks larger than a MAN. It has wide spread every where. Internet is example of WAN. Its range is unlimited.

## Slide 17: 3. On the basis of its architecture
Network architecture: is a design & organization of a network or computer system. Architecture can be broadly classified into two ways.
1 . Peer to peer architecture
This is a type of network in which each work station has equivalent capabilities & responsibilities. It is simpler & less expensive but they do not offer the same performance under heavy load.
2 . Client server architecture
This is a network architecture in which each computer on the network is either a client or a server. Servers are powerful computers which manages files, servers network server etc. clients are less powerful work stations or pc on which users run applications. Clients rely on servers for resources such as files, devices etc.

## Slide 18: Communication media
Channels are also called communication lines or links are the means by which data is transmitted between the sending & receiving devices in a network. A channels are twisted pair wire, coaxial cable & fiber optics which physically link the devices in a network.
Two types of media.
Bounded media
Unbounded media

## Slide 19
Bounded media
Twisted pair wire: This is the oldest & still common transmission line consists of copper wires twisted into pairs. It is also called UTP(unshielded twisted pair). UTP cables are used commonly in local telecommunication & short distance digital data transmission. UTP cables are inexpensive, easy to install & use.
2. Coaxial cable : It is a groups of specially wrapped & insulated wire lines capable of transmitting data at high rates. coaxial cables offer much higher band width(Signal processing(frequency ,radio etc.) than UTP cables & can transmit digital signals at rates up to 10 Mbps.

## Slide 20
3. Fiber optics or optical fiber : Optical fibers are thin threads of glass or plastic used as data transmission medium like copper wires or coaxial cables they transmit light signals instead of electrical signals. So, light travels much faster than electricity. Optical fibers can transmit data at much higher speed than coaxial cables.
Advantages
Large band width
Low loss
Small size & light weight

## Slide 21
2. Unbounded media
Unbounded media are satellite, microwave, Wi - Fi , Blue tooth etc.
Satellite : Satellite is space orbiting 2200 miles above the earth ,are also used as microwave relay stations . It is also suitable for long distance communications. They are powered by solar panels and carry different types of signals ,such as standard television broadcasting, telephone transmissions and high speed data.

## Slide 22
Microwave :Earth bound microwave systems transmit high speed radio signals in a line of sight path between relays stations spaced approximately 25 to 35 miles apart. They are consists of antennas usually placed on the top of buildings, towers & hills etc. Microwave radios are useful for connecting networks that are only short distances apart.
  Wi-Fi : Wi-Fi stands for wireless fidelity. It is a world wide. Wi–Fi technology uses radio for communication ,typically operating at a frequency of 24 GHZ. PDA ,laptops and various accessories are designed to be Wi-Fi.

## Slide 23
Bluetooth : A proposed radio frequency specification that many portable devices will use for short – range wireless communication is called Bluetooth. With Bluetooth , devices such as laptop computers, handheld computers, cellular telephones,pagers,fax machines and printers can wirelessly communicate with each other ,desktop computers ,a network or the internet.

## Slide 24: Functions of telecommunications software
Access control
Transmission control
Network control
Error control
Security control

## Slide 25: Network Topology
The geometrical arrangement of a computer system is called topology. In other words, topology of a network refers to the way in which the networks nodes are linked together. Topology can be divided into six ways.
1. Bus topology
2. Star topology
3. Ring topology
4. Mesh topology
5. Hybrid topology
6. Tree topology

## Slide 26
Bus topology
In bus topology, all the nodes share a single transmission medium. That is ,all nodes are attached to the same communication line or channel.This type of network is also known as multipoint network or broadcast network. It is appropriate for LAN where a high speed communication channel is used.

## Slide 27
Advantages
It reducing the number of physical lines.
Failure of a node does not affect communication among other nodes in the network.
Addition of new nodes to the network is easy.
Disadvantages
If the shared communication line fails then network fails.
All nodes in a network must have good communication & decision making capabilities.

## Slide 28
2. Star topology
The nodes in the network are linked to each other through the host node & can communicate only the host node.
Advantages
If any node other than the host node fails, remaining nodes are unaffected.
hub

## Slide 29
Disadvantages
The system depends on host node if it fails then network also fails.
3. Ring topology
It is also known as circular topology. In ring topology ,each node has two communicating adjacent nodes with which it can communicate directly ,but there is no master node for controlling other nodes.
Advantages
It works well where there is no central nodes for making routing decisions.

## Slide 30
Disadvantages
It requires more complicated control software than star topology.

## Slide 31
Disadvantages
It is the most expensive network from the point of view of link cost.

## Slide 32
4. Mesh topology is a completely connected network. It has a separate physical link for connecting each node to any other node.
Advantages
Each node of the network need not have individual routing capability.
Communication is very fast between any two nodes.
Disadvantages
It is the most expensive network from the point of view of link cost.

## Slide 33
5.Hybrid topology
Hybrid network is a combination of two or more different network topologies. Exact configuration of a network depends needs & structure of the organization. It is the combination of multiple network.

## Slide 34
Disadvantages
It is the combination of multiple network. most expensive network from the point of view of link cost.
Tree topology
In a tree topology , each device is connected to its own port or hub just like a star topology. Tree topology interconnects hub in hierarchical way.
Advantages
It is easy to extend because tree topology is divided into many sub units.
Easy to add new nodes.
If hub is failure then network continues to operate.
Disadvantage
The network depends on the root.

## Slide 35: Communication systems
Communication is the transmission of data from one computer to another. As for example Radio, TV , Satellite, Radar etc.
Radar
The name ‘radar’ is the acronym of Radio Detecting & Ranging. It denotes the method of scanning the surrounding space by means of high frequency radio waves, which are sent out from a powerful transmitter & are reflected by any objects.

## Slide 36: ISDN(Integrated Services Digital Network)
Already discussed

## Slide 37: Satellite
Already discussed.

## Slide 38: Distributed systems
Earlier times, most of the data are stored in a central part. This process is called centralized process or system.
But in distributed system, the computers, storage devices are distributed to separate locations. T his system can be more responsive to its users, needs low cost to develop & maintain the data easily.

## Slide 39: Advantages
Local control of data.
Lower cost.
Better response times.
Ability to share data.
Greater reliability.
Direct user interaction.

## Slide 40: Disadvantages
Need for sophisticated communication systems.
Data integrity & security problems.
Lack of professional support.
Technical problems of connecting dissimilar machines.